## Slide 1: WELCOME!
Girl Develop It is here to provide affordable and accessible programs to learn software through mentorship and hands-on instruction.
Some "rules"
We are here for you!
Every question is important
Help each other
Have fun

## Slide 2: Upcoming Events
Oct 24 – Into to Arduino and Robotics Class
  4hrs *$30.00
Nov 1 – Code & Coffee (free)
2016
  Introduction to HTML and CSS
  Introduction to Programming with Python
  Introduction to Databases and SQL (I & II)
  More!

## Slide 3: Introduction to 3D Printing
“ I want to say one word to you. Just one word.…
Plastics”
The Graduate - 1967

## Slide 4: Introductions
Name
Favorite ice cream or desert

## Slide 5: What is 3D Printing
Additive Manufacturing (Legos)
  Subtractive (carving, milling)
Material is pushed through a nozzle (extruded)
  Filament is heated to allow this to happen
  Icing or pastry bag

## Slide 6: Uses for 3D Printers
Prototyping
Small lot manufacturing (cookie cutters)
Specialized or hard to find items (car parts)
Education (music, animals)
To be determined!

## Slide 7: My Favorite Thing
It was a Saturday morning….

## Slide 8: 3D Pinter Types
Cartesian
Delta
DLP

## Slide 9: Cartesian

## Slide 10: Delta

## Slide 11: Delta Style Printer (video)
(https://www.youtube.com/watch?feature=player_embedded&v=zQxa920YGaU )

## Slide 12: DLP

## Slide 13: DLP Style Printer
(https://www.youtube.com/watch?feature=player_embedded&v=nxhUjPmxrP0 )

## Slide 14: Money, Money, Money
Overall price range $500 - $2500+
Why the difference?
Technology (type) and build volume.

## Slide 15: Differences
Technology (material)
  Filament
    PLA ($500 kit)
    ABS (heated bed) (+$100)
    Assembled (+$150)
    Dual Head (+$200)
  Resin (DLP)

## Slide 16: Differences
Build Volume
  4” x 4” x 4” ($400)
  10” x 10” x 10” ($1000+)
  7” x 15” x 7” DLP ($2500+)

## Slide 17: Filament
Size 1.75mm (standard) & 3.00mm (old)
Material
  PLA (Strong, stiff, fast print)
  ABS (Heated bed, higher temp, slight flex)
  Flex (rubber like)

## Slide 18: Filament Exotics
Material
  Nylon (Very Strong, very high print temp)
  Wood
  Conductive
  Metallic (bronze, iron, etc)
  Ceramic

## Slide 19: What to Print?
You need a 3D model (.stl file)
  Use an existing model
    www.thingiverse.com
  Make your own model
    Tinkercad (web based www.tinkercad.com )
    Meshmixer
    Blender (open source)
    Autocad 123D Design

## Slide 20: How to Print?
3D printers use GCode
  Set of instructions (movement, speed, temp, etc)
(**** start.gcode for The Replicator, dual head ****)
M103 (disable RPM)
M73 P0 (enable build progress)
G21 (set units to mm)
G90 (set positioning to absolute)
M109 S065 T0 (set HBP temperature)
M104 S220 T0 (set extruder temperature) (temp updated by printOMatic)
…
G1 X-29.91 Y-29.91 Z0.1 F1080.0 E1.0
G1 X-23.5 Y-35.17 Z0.1 F1080.0 E1.3
G1 X-16.19 Y-39.08 Z0.1 F1080.0 E1.6
G1 X-8.25 Y-41.49 Z0.1 F1080.0 E1.9

## Slide 21: Slicers
Convert Models to GCode
  Skeinforge used in ReplicatorG (oldie but a goodie)
  Repetier (includes Slic3r )
  Slic3r
  KISSlicer
  Makerware (Makerbot)
  Simplify3D ($$$)

## Slide 22: Terminology / Settings
Layer Height
Shells
Infill
Support
Skirt (brim)
Raft

## Slide 23: Terminology / Settings
Layer Height
  0.1 mm, (fine)
  0.2 mm, (med)
  0.3 mm (coarse)

## Slide 24: Bed Leveling is Important
Layer height (0.1, 0.2, 0.3mm)
  1/64” ~ 0.4mm
  Sheet of paper is ~ 0.05mm thick

## Slide 25: Terminology / Settings
Shells –
  How many layers around the outside
  1,2,…? (2 is common, 4 or more extreme)

## Slide 26: Terminology / Settings
Infill –
  10% - 100%
  10% - 20% is common

## Slide 27: Infill
10%
40%

## Slide 28: Terminology / Settings
Support
  Printed material that is not part of the finished model
  scaffolding

## Slide 29: Support
Overhangs

## Slide 30: Terminology / Settings
Skirt (brim)
Raft
These are both used to help the model stick to the build platform and reduce warping

## Slide 31: Skirt / Brim
Top
Bottom

## Slide 32: Raft
Top
Bottom

## Slide 33: Stick It
First layer is the most important layer
Getting the first layer to adhere to the print bed
  Painters tape (blue tape) – PLA only
  Glass with hairspray
  Kapton tape
  ABS juice (ABS and acetone)

## Slide 34: Danger! Danger! Will Robinson!
Plastic | Bed / Table |  | Nozzle | 
 | C | F | C | F
PLA | 0 – 65 | 0 - 149 | 200 - 210 | 392 – 410
ABS | 110 – 115 | 230 - 239 | 225 - 235 | 437 - 455

## Slide 35: Common Tools

## Slide 36: How Many ‘x’ Can I Print?
Matter is neither created nor destroyed
A standard spool of filament is 1kg (2.2 pounds)
Ukulele weighs about 425g (0.425kg) so it took just under half a spool of filament.
A cookie cutter weighs < 10g
  1000g / 10 = 100 so you can print about 100 cookie cutters from a single 1kg (1000g) spool of filament.

## Slide 37: Questions!