## Slide 1: Introduction to 3D Printing
“ I want to say one word to you. Just one word.…
Plastics”
The Graduate - 1967

## Slide 2: Introductions
Name
Favorite ice cream or desert

## Slide 3: What is 3D Printing
Additive Manufacturing (Legos)
  Subtractive (carving, milling)
Material is pushed through a nozzle (extruded)
  Filament is heated to allow this to happen
  Icing or pastry bag
  Hot Glue gun

## Slide 4: Uses for 3D Printers
Prototyping
Small lot manufacturing (cookie cutters)
Specialized or hard to find items (car parts)
Education (music, animals)
To be determined!

## Slide 5: My Favorite Thing
It was a Saturday morning….

## Slide 6: 3D Pinter Types
Cartesian
Delta
DLP

## Slide 7: Cartesian

## Slide 8: Delta

## Slide 9: Delta Style Printer (video)
(https://www.youtube.com/watch?feature=player_embedded&v=zQxa920YGaU )

## Slide 10: DLP

## Slide 11: DLP Style Printer
(https://www.youtube.com/watch?feature=player_embedded&v=nxhUjPmxrP0 )

## Slide 12: Money, Money, Money
Overall price range $300 - $2500+
Why the difference?
Technology (type) and build volume.

## Slide 13: Money, Money, Money
FREE!
Boise Public Library
  Online sign-up 2 hour slots
Meridian Library District (Unbound)
  Send them your model

## Slide 14: Differences
Technology (material)
  Filament
    PLA ($300 kit)
    ABS (heated bed) (+$100)
    Assembled (+$150)
    Dual Head (+$200)
  Resin (DLP)

## Slide 15: Differences
Build Volume
  4” x 4” x 4” ($300)
  10” x 10” x 10” ($1000+)
  7” x 15” x 7” DLP ($2500+)

## Slide 16: Filament
Size 1.75mm (standard) & 3.00mm (old)
Material
  PLA (Strong, stiff, fast print)
  ABS (Heated bed, higher temp, slight flex)
  Flex (rubber like)

## Slide 17: Filament Exotics
Material
  Nylon (Very Strong, very high print temp)
  Wood
  Conductive
  Metallic (bronze, iron, etc)
  Ceramic

## Slide 18: What to Print?
You need a 3D model (.stl file)
  Use an existing model
    www.thingiverse.com
  Make your own model
    Tinkercad (web based)
    OnShape (web based)
    Meshmixer
    Blender (open source)
    Autocad 123D Design
    openSCAD (open source; code based)

## Slide 19: How to Print?
3D printers use GCode
  Set of instructions (movement, speed, temp, etc)
(**** start.gcode for The Replicator, dual head ****)
M103 (disable RPM)
M73 P0 (enable build progress)
G21 (set units to mm)
G90 (set positioning to absolute)
M109 S065 T0 (set HBP temperature)
M104 S220 T0 (set extruder temperature) (temp updated by printOMatic)
…
G1 X-29.91 Y-29.91 Z0.1 F1080.0 E1.0
G1 X-23.5 Y-35.17 Z0.1 F1080.0 E1.3
G1 X-16.19 Y-39.08 Z0.1 F1080.0 E1.6
G1 X-8.25 Y-41.49 Z0.1 F1080.0 E1.9

## Slide 20: Slicers
Convert Models to GCode
  Cura (Ulitmaker)
  Repetier (includes Slic3r )
  Skeinforge used in ReplicatorG (oldie but a goodie)
  KISSlicer
  Makerware (Makerbot)
  Simplify3D ($$$)

## Slide 21: Terminology / Settings
Layer Height
Shells
Infill
Support
Skirt (brim)
Raft

## Slide 22: Terminology / Settings
Layer Height
  0.1 mm, (fine)
  0.2 mm, (med)
  0.3 mm (coarse)

## Slide 23: Bed Leveling is Important
Layer height (0.1, 0.2, 0.3mm)
  1/64” ~ 0.4mm
  Sheet of paper is ~ 0.05mm thick

## Slide 24: Terminology / Settings
Shells –
  How many layers around the outside
  1,2,…? (2 is common, 4 or more extreme)

## Slide 25: Terminology / Settings
Infill –
  10% - 100%
  10% - 20% is common

## Slide 26: Infill
10%
40%

## Slide 27: Terminology / Settings
Support
  Printed material that is not part of the finished model
  scaffolding

## Slide 28: Support
Overhangs

## Slide 29: Terminology / Settings
Skirt (brim)
Raft
These are both used to help the model stick to the build platform and reduce warping

## Slide 30: Skirt / Brim
Top
Bottom

## Slide 31: Raft
Top
Bottom

## Slide 32: Stick It
First layer is the most important layer
Getting the first layer to adhere to the print bed
  Painters tape (blue tape) – PLA only
  Glass with hairspray
  Kapton tape
  ABS juice (ABS and acetone)

## Slide 33: Danger! Danger! Will Robinson!
Plastic | Bed / Table |  | Nozzle | 
 | C | F | C | F
PLA | 0 – 65 | 0 - 149 | 200 - 210 | 392 – 410
ABS | 110 – 115 | 230 - 239 | 225 - 235 | 437 - 455

## Slide 34: Common Tools

## Slide 35: How Many ‘x’ Can I Print?
Matter is neither created nor destroyed
A standard spool of filament is 1kg (2.2 pounds)
Ukulele weighs about 425g (0.425kg) so it took just under half a spool of filament.
A cookie cutter weighs < 10g
  1000g / 10 = 100 so you can print about 100 cookie cutters from a single 1kg (1000g) spool of filament.

## Slide 36: Questions!