## Slide 1: Introduction to 3D Printing
“ I want to say one word to you. Just one word.…
Plastics”
The Graduate - 1967

## Slide 2: WELCOME!
Girl Develop It is here to provide affordable and accessible programs to learn software through mentorship and hands-on instruction.
Some "rules"
We are here for you!
Every question is important
Help each other
Have fun

## Slide 3: Introductions
Name
Favorite ice cream or desert

## Slide 4: My Favorite Thing
It was a Saturday morning….

## Slide 5: 3D Pinter Types
Cartesian
Delta
DLP

## Slide 6: Cartesian

## Slide 7: Delta

## Slide 8: Delta Style Printer (video)

## Slide 9: DLP

## Slide 10: DLP Style Printer

## Slide 11: Money, Money, Money
Overall price range $500 - $2500+
Why the difference?
Technology (type) and build volume.

## Slide 12: Differences
Technology (material)
  Filament
    PLA ($500 kit)
    ABS (heated bed) (+$100)
    Assembled (+$150)
    Dual Head (+$200)
  Resin (DLP)

## Slide 13: Differences
Build Volume
  4” x 4” x 4” ($400)
  10” x 10” x 10” ($1000+)
  7” x 15” x 7” DLP ($2500+)

## Slide 14: Filament
Size 1.75mm (standard) & 3.00mm (old)
Material
  PLA (Strong, stiff, fast print)
  ABS (Heated bed, higher temp, slight flex)
  Flex (rubber like)

## Slide 15: Filament Exotics
Material
  Nylon (Very Strong, very high print temp)
  Wood
  Conductive
  Metalic (bronze, iron, etc)
  Ceramic

## Slide 16: What to Print?
You need a 3D model (.stl file)
  Use an existing model
    www.thingiverse.com
  Make your own model
    Tinkercad (web based www.tinkercad.com )
    Meshmixer
    Blender (open source)
    Autocad 123D Design

## Slide 17: How to Print?
3D printers use GCode
  Set of instructions (movement, speed, temp, etc)
(**** start.gcode for The Replicator, dual head ****)
M103 (disable RPM)
M73 P0 (enable build progress)
G21 (set units to mm)
G90 (set positioning to absolute)
M109 S065 T0 (set HBP temperature)
M104 S220 T0 (set extruder temperature) (temp updated by printOMatic)
…
G1 X-29.91 Y-29.91 Z0.1 F1080.0 E1.0
G1 X-23.5 Y-35.17 Z0.1 F1080.0 E1.3
G1 X-16.19 Y-39.08 Z0.1 F1080.0 E1.6
G1 X-8.25 Y-41.49 Z0.1 F1080.0 E1.9

## Slide 18: Slicers
Convert Models to GCode
  Skeinforge used in ReplicatorG (oldie but a goodie)
  Slic3r
  KISSlicer
  Makerware (Makerbot)
  Simplify3D ($$$)

## Slide 19: Terminology / Settings
Layer Height - 0.1, 0.2, 0.3 mm (fine, med, coarse)
Shells - 1,2,…? (2 is common, 4 or more extreme)
Infill -10% - 100% (20% is common)
Support
Skirt (brim)
Raft

## Slide 20: Infill
10%
40%

## Slide 21: Support
Overhangs

## Slide 22: Raft
Top
Bottom

## Slide 23: Skirt / Brim
Top
Bottom

## Slide 24: Danger! Danger! Will Robinson!
Top
Bottom
Plastic | Bed / Table |  | Nozzle | 
 | C | F | C | F
PLA | 0 – 65 | 0 - 149 | 200 - 210 | 392 – 410
ABS | 110 – 115 | 230 - 239 | 225 - 235 | 437 - 455