## Slide 1: Upcoming GDI Events at Trailhead
July 12, 1:00 – 3:00 pm Code & Coffee
July 15, 5:30 – 7:30 pm Intro to Databases & SQL

## Slide 2: Introduction to 3D Printing
“ I want to say one word to you. Just one word.…
Plastics”
The Graduate - 1967

## Slide 3: WELCOME!
Girl Develop It is here to provide affordable and accessible programs to learn software through mentorship and hands-on instruction.
Some "rules"
We are here for you!
Every question is important
Help each other
Have fun

## Slide 4: Introductions
Name
Favorite ice cream or desert

## Slide 5: What is 3D Printing
Additive Manufacturing (Legos)
  Subtractive (carving, milling)
Material is pushed through a nozzle (extruded)
  Filament is heated to allow this to happen
  Icing or pastry bag

## Slide 6: Uses for 3D Printers
Prototyping
Small lot manufacturing (cookie cutters)
Specialized or hard to find items (car parts)
Education (music, animals)
To be determined!

## Slide 7: My Favorite Thing
It was a Saturday morning….

## Slide 8: 3D Pinter Types
Cartesian
Delta
DLP

## Slide 9: Cartesian

## Slide 10: Delta

## Slide 11: Delta Style Printer (video)

## Slide 12: DLP

## Slide 13: DLP Style Printer

## Slide 14: Money, Money, Money
Overall price range $500 - $2500+
Why the difference?
Technology (type) and build volume.

## Slide 15: Differences
Technology (material)
  Filament
    PLA ($500 kit)
    ABS (heated bed) (+$100)
    Assembled (+$150)
    Dual Head (+$200)
  Resin (DLP)

## Slide 16: Differences
Build Volume
  4” x 4” x 4” ($400)
  10” x 10” x 10” ($1000+)
  7” x 15” x 7” DLP ($2500+)

## Slide 17: Filament
Size 1.75mm (standard) & 3.00mm (old)
Material
  PLA (Strong, stiff, fast print)
  ABS (Heated bed, higher temp, slight flex)
  Flex (rubber like)

## Slide 18: Filament Exotics
Material
  Nylon (Very Strong, very high print temp)
  Wood
  Conductive
  Metalic (bronze, iron, etc)
  Ceramic

## Slide 19: What to Print?
You need a 3D model (.stl file)
  Use an existing model
    www.thingiverse.com
  Make your own model
    Tinkercad (web based www.tinkercad.com )
    Meshmixer
    Blender (open source)
    Autocad 123D Design

## Slide 20: How to Print?
3D printers use GCode
  Set of instructions (movement, speed, temp, etc)
(**** start.gcode for The Replicator, dual head ****)
M103 (disable RPM)
M73 P0 (enable build progress)
G21 (set units to mm)
G90 (set positioning to absolute)
M109 S065 T0 (set HBP temperature)
M104 S220 T0 (set extruder temperature) (temp updated by printOMatic)
…
G1 X-29.91 Y-29.91 Z0.1 F1080.0 E1.0
G1 X-23.5 Y-35.17 Z0.1 F1080.0 E1.3
G1 X-16.19 Y-39.08 Z0.1 F1080.0 E1.6
G1 X-8.25 Y-41.49 Z0.1 F1080.0 E1.9

## Slide 21: Slicers
Convert Models to GCode
  Skeinforge used in ReplicatorG (oldie but a goodie)
  Slic3r
  KISSlicer
  Makerware (Makerbot)
  Simplify3D ($$$)

## Slide 22: Terminology / Settings
Layer Height - 0.1, 0.2, 0.3 mm (fine, med, coarse)
Shells - 1,2,…? (2 is common, 4 or more extreme)
Infill -10% - 100% (10% - 20% is common)
Support
Skirt (brim)
Raft

## Slide 23: Infill
10%
40%

## Slide 24: Support
Overhangs

## Slide 25: Skirt / Brim
Top
Bottom

## Slide 26: Raft
Top
Bottom

## Slide 27: Danger! Danger! Will Robinson!
Plastic | Bed / Table |  | Nozzle | 
 | C | F | C | F
PLA | 0 – 65 | 0 - 149 | 200 - 210 | 392 – 410
ABS | 110 – 115 | 230 - 239 | 225 - 235 | 437 - 455

## Slide 28: Bed Leveling is Important
Layer height (0.1, 0.2, 0.3mm)
  1/64” = 0.3969mm
  Sheet of paper is ~ 0.05mm thick

## Slide 29: Stick It
First layer is the most important layer
Getting the first layer to adhere to the print bed
  Painters tape (blue tape) – PLA only
  Glass with hairspray
  Kapton tape
  ABS juice (ABS and acetone)

## Slide 30: How Many ‘x’ Can I Print?
Matter is neither created nor destroyed
A standard spool of filament is 1kg (2.2 pounds)
Ukulele weighs about 425g (0.425kg) so it took just under half a spool of filament.
A cookie cutter weighs < 10g
  1000g / 10 = 100 so you can print about 100 cookie cutters from a single 1kg (1000g) spool of filament.